SAMPLE POLICY

VEHICLE BACKING

(Organization)

Purpose:

The purpose of this document is to set policy for the backing of all vehicles and to standardize the signals for backing.

Policy:

It shall be the policy of  (Organization) that backing of vehicles shall be avoided whenever possible.  Where backing is unavoidable, a spotter shall be utilized.  In addition, a spotter shall be used when vehicles must negotiate forward turns with restrictive side clearances and where height clearances are uncertain.

Guidelines:

When a company vehicle is to be backed, one employee shall get out of and act as a spotter.  This employee will be located off the left rear corner, visible to the driver in the side mirror.

The spotter shall review the backing plan with the driver and agree to the communication process before proceeding.  Both door windows shall be open to allow for proper communication and fire radio volumes reduced.

The vehicle shall not begin backing until the spotter is in position and communicates approval to begin.  Anytime the driver losses sight of the spotter, the vehicle shall be immediately stopped.

The spotter shall be responsible to check clearances on all sides including overhead.

Signals:

Straight Back: Both hands above the head with the palm away from the driver, waving back.

Turn:  Both arms pointing in the same direction with index fingers extended.

Stop:  Both arms crossed with the hands in a fist.

All hand signals shall be accompanied by verbal signals.

For further information on formulation of your business policies and procedures, please contact the Risk Management Department at 1-800-822-3747 Ext. 176.